## Slide 1: Microprocessor & Computer Architecture UE17CS253
UNIT-2
Session – 8
Performance Metrics, trends in Technology, Power and Energy

## Slide 2: Performance Metrics
Performance:
  A quantifiable measure of rate of doing (computational) work
  Multiple such measures of performance
    Delineated at the level of the basic operation
      ops – operations per second
      ips – instructions per second
      flops – floating operations per second
    Rate at which a benchmark program takes to execute
      A carefully crafted and controlled code used to compare systems
      Linpack Rmax (Linpack flops)
      gups (billion updates per second)
      others
Two perspectives on performance
  Peak performance
    Maximum theoretical performance possible for a system
  Sustained performance
    Observed performance for a particular workload and run
    Varies across workloads and possibly between runs

## Slide 3: Trends in Technology
Integrated circuit technology
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
  Moore’s law: #transistors/sq inch doubled every 2 years
DRAM capacity: 25-40%/year (slowing)
Flash capacity: 50-60%/year
  15-20X cheaper/bit than DRAM
Magnetic disk technology: 40%/year
  15-25X cheaper/bit then Flash
  300-500X cheaper/bit than DRAM
Trends in Technology

## Slide 4: The PowerPlay

## Slide 5: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .032 microns in 2011
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically
Trends in Technology

## Slide 6: Power and Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power, higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement
Trends in Power and Energy

## Slide 7: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 -> 1 or 1 -> 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency switched
Reducing clock rate reduces power, not energy
Trends in Power and Energy

## Slide 8: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air
Trends in Power and Energy

## Slide 9: Reducing Power
Techniques for reducing power:
  Do nothing well
  Dynamic Voltage-Frequency Scaling
  Low power state for DRAM, disks
  Overclocking, turning off cores
Trends in Power and Energy

## Slide 10: Static Power
Static power consumption
  Currentstatic x Voltage
  Scales with number of transistors
  To reduce: power gating
Trends in Power and Energy